## Slide 1: CALIPSO Introduction
Jennifer D. S. Griswold
MET 611 – Satellite Data Applications
Many slides are from a talk by Meloë Kacenelenbogen, Mark Vaughan, and Jens Redemann for a NASA ARSET- AQ DRI Course June 11 - 14, 2012

## Slide 2: CALIPSO
The Cloud-Aerosol Lidar and Infrared Pathfinder Satellite Observation (CALIPSO)
Launched April 28 2006 with CloudSat
Provides new insight into:
  The role that clouds and atmospheric aerosols (airborne particles) play in regulating Earth's weather, climate, and air quality.
  With Cloudsat – 3D perspective on cloud-aerosol interactions
  How clouds and aerosols form and evolve
  Weather and climate studies
Combines an active lidar instrument with passive infrared and visible imagers to probe:
  vertical structure and properties
  Focus on: thin clouds and aerosols over the globe.

## Slide 3
Joint NASA/CNES satellite
Three instruments:
  Cloud-Aerosol Lidar with Orthogonal Polarization (CALIOP): Two wavelength polarization-sensitive Lidar that provides high-resolution vertical profiles of aerosols and clouds
  Wide Field Camera (WFC): Fixed, nadir-viewing imager with a single spectral channel covering the 620-670 nm region
  Imaging Infrared Radiometer (IIR): Nadir-viewing, non-scanning imager
CALIPSO - CALIOP
Rhymes with “eye-oh-pee”

## Slide 4
705 km, sun-synchronous
CALIOP:
backscatter Nd:YAG lidar
532, 532-perp, 1064
Launch: 28 April 2006
Active downward pointing elastic backscatter LIDAR (LIght Detection And Ranging)
90 m diameter foot print every 333m; No daily global coverage, covers a given region every 16 days

## Slide 5: How does CALIOP work?
scattering layer
1064,Total
532,Total
532,⊥
Total = || + ⊥
1
Total backscatter coefficient (cloud, aerosol, molecule)
2
LIDAR signal
3
Attenuated backscatter coefficient
4
Atmospheric two-way transmittance
= signal attenuation (cloud, aerosol, molecule, gas)

## Slide 6: Important Points to Know about CALIOP
Lidar signal β’
Aerosol and molecular backscatter
Is a function of extinction and backscatter
LIDAR Ratio Sa = αa/βa Aerosol extinction-to-backscatter ratio
(Assumed for CALIOP)
Color Ratio The ratio of the short to long wavelength.
Gives information on particle size.
For multiple wavelength lidars.

## Slide 7: Lidar Signal Interpretation
A
B
Total attenuated backscatter 532 nm
Total attenuated backscatter 1064 nm
 |  |  | Particle Type
Enhanced Signal | Enhanced Signal | Same intensity as 532 | Non-Spherical Coarse
Enhanced Signal | Enhanced Signal | Lower intensity than 532 | Non-Spherical Fine
Enhanced Signal | Non Enhanced Signal | Same intensity as 532 | Spherical Coarse
Enhanced Signal | Non Enhanced Signal | Lower intensity than 532 | Spherical Fine

## Slide 8: Tracks per 5x5 grid cell over 16 days
50
23

## Slide 9: Penetration Statistics
Zonal average penetration frequency (5-km average profiles)
Global average (single shots) CALIPSO
6 km 58%
4 km 52
2 km 43
Sfc 31
CALIPSO
orbit 705 km
energy 110 mJ

## Slide 10
CALIPSO
“Curtain”
“/km /sr” - per km per steradian (square radian)
Notes: Backscattering can occur in quite different physical situations, where the incoming waves or particles are deflected from their original direction by different mechanisms:
Diffuse reflection from large particles and Mie scattering, causing alpenglow and gegenschein, and showing up in weather radar;
inelastic collisions between electromagnetic waves and the transmitting medium (Brillouin scattering and Raman scattering), importa

## Slide 11
Planetary Boundary Layer
Free Troposphere
Troposphere
clouds
Land
aerosols
PBL
532 nm
5km -
10km -
15km -
20km -
25km -
0km -
Longitude
Latitude
What’s a CALIPSO Curtain Scene?

## Slide 12: CALIPSO products
Version 3.3 Product | Primary Parameter | Resolution due to averaging | 
 |  | Horizontal | Vertical (<8km)
Level 1 Measured | Total_Attenuated_Backscatter_532 Perpendicular_Attenuated_Backscatter_532 Total_Attenuated_Backscatter_1064 | 1/3km | 30m
Level 2 LAYER Retrieved | Cloud Layer_Top/ Base_Altitude | 1/3, 1, 5km | 30m
 | Aerosol Layer_Top/ Base_Altitude | 5km | 30m
Level 2 PROFILE Retrieved | Cloud and Aerosol Total_Backscatter_Coefficient_532 Extinction_Coefficient_532 | 5km | 60m
Level 2 Vertical Feature Mask Retrieved | Feature_Classification_Flags | 5km | 30m

## Slide 13: Lidar Data Products
Level 1 (geolocated and calibrated)
DP 1.1 - profiles of attenuated lidar backscatter (532, 532^, 1064 nm)
DP 1.2 – IR radiances (8.65, 10.6, 12.05 mm)
DP 1.3 – Visible radiances (650 nm) (WFC)
Level 2
DP 2.1A – Cloud/Aerosol layer product
  layer base and top heights, layer-integrated properties
DP 2.1B – Aerosol profile product
  backscatter, extinction, depolarization profiles
DP 2.1C – Cloud profile product
  backscatter, extinction, depolarization, ice/water content profiles
DP 2.1D – Vertical Feature mask
  cloud/aerosol locations
(available at https://eosweb.larc.nasa.gov/project/calipso/calipso_table

## Slide 14: From lidar signal to extinction profile? -Theory-
Molecular backscatter and attenuation can be computed
=> β’ function of βa and αa
In a cloud-free atmosphere:
For aerosols:
Aerosol extinction coefficient
If we assume an aerosol extinction-to-backscatter LIDAR ratio Sa= αa/βa
function of particle size and shape and β’ in 3 channels
=> Retrieval of βa and αa
One measurement
Two unknowns
=> calibration => Attenuated backscatter coefficient β’
Lidar signal
Aerosol and molecular backscatter
Atmospheric two-way transmittance
= signal attenuation
Aerosols, Molecules, Ozone

## Slide 15: Layer classification
a) Cloud-Aerosol Discrimination [Liu et al., 2004, 2009]
b) Cloud ice-water phase discrimination [Hu et al., 2009]
Look Up Table | 
Aerosol Sub-type | Initial Sa,532
biomass burning smoke | 70
polluted dust | 65
polluted continental | 70
clean continental | 35
desert dust | 40
marine | 20
c) Aerosol sub-typing and observation-based lidar ratio Sa:
[Omar et al., 2005, 2009; Liu et al., 2009]

## Slide 16: CALIPSO validation
Level 1 CALIOP attenuated backscatter
Absence of evident bias in CALIOP level 1 attenuated backscatter profiles
CALIOP 532 nm calibration algorithm seems fairly accurate
  1. Ground-based validation with EARLINET (European Aerosol Research LIdar NETwork):
  Relative mean difference of ~4.6% between CALIOP and EARLINET since June 2006 over Europe [Pappalardo et al., 2010]
      2. Airborne validation with HSRL (High Spectral Resolution Lidar):
      HSRL and CALIOP (coincident data from 86 underflights) agree on average within 2.7±2.1% (CALIOP lower) at night and within 2.9±3.9% (CALIOP lower) during the day [Rogers et al., 2010]
EARLINET
HSRL flights

## Slide 17: CALIPSO validation
Level 2 CALIOP layer boundaries, backscatter and extinction
Very little validation of CALIOP level 2 data: few case studies
Significant uncertainties associated with level 2 data
1. Ground-based validation with EARLINET
Example: CALIPSO underestimates Sa (40 instead of ~50 sr, hence underestimates AOD) during 26–31 May 2008 Saharan Dust outbreak [Pappalardo et al., 2010]
2. Airborne validation with HSRL
CALIOP overestimates HSRL extinction with an average extinction bias of ~ 24% during CATZ (CALIPSO and Twilight Zone campaign) and ~59% during GoMACCS (Gulf of Mexico Atmospheric Composition and Climate Study) [Omar et al, 2009]

## Slide 18: CALIPSO validation
3. CALIOP versus other A-Train satellite AOD
  CALIOP (V3.01) better than CALIOP (V2)-MODIS AOD but still not satisfactory
  CALIOP (V3.01) globally overestimates MODIS AOD over ocean with R2=0.30 in January 2007
CALIOP Version 2
CALIOP Version 3.01
[Redemann et al., in prep.]
[Redemann et al., in prep.]
R2=0.17
R2=0.30
  CALIOP (V2) underestimates both POLDER and MODIS AOD (also AERONET and HSRL) on August 04 2007 by 0.1-0.2 during CATZ [Kacenelenbogen et al., 2010]

## Slide 19: CALIPSO validation
Additional cloud-screening on both datasets with MODIS cloud fraction
CALIOP Version 3.01
R2=0.52
Reduces discrepancies between two data sets due to cloud contamination
Higher correlation coefficient (0.52 instead of 0.30)
CALIPSO slightly underestimates MODIS AOD

## Slide 20: Level 2 data uncertainties
Low Signal to noise ratio
CALIOP will fail to detect layers with aerosol backscatter < 2~4 10-4 km-1 sr-1 in troposphere [Winker et al., 2009] (Sa of 50sr, α of 0.01-0.02 km-1, AOD of 0.02-0.04 in 2km)
CALIOP not measuring tenuous aerosol layers
 Lack of photons returned from underneath highly attenuating layers (dense aerosol or cloud) leading to erroneous or total lack of aerosol identification in the lower part of a given atmospheric profile
Miss-classification of layer type (aerosol or cloud) and aerosol sub-type (biomass, dust, etc…)
 leading to incorrect assumption about lidar ratio Sa
Improved calibration technique
 for the lidar Level 1 532 nm daytime calibration in Version 3.01 [Powell et al., 2010]
Multiple scattering is assumed negligible in current algorithm
 Impact on cases with dense dust plumes recording high AOD where effects of multiple scattering applies

## Slide 21: CALIPSO browse images online
If enhanced signal in both images then non spherical particles (Region A)
If enhanced signal in total backscatter image but little or no enhancement in the perpendicular image, then spherical particles (Region B)
A
B
A
B
Level 1 products
Total attenuated backscatter 532 nm
Perpendicular attenuated backscatter 532 nm

## Slide 22: Lidar Signal Interpretation
A
B
Total attenuated backscatter 532 nm
Total attenuated backscatter 1064 nm
 |  |  | Particle Type
Enhanced Signal | Enhanced Signal | Same intensity as 532 | Non-Spherical Coarse
Enhanced Signal | Enhanced Signal | Lower intensity than 532 | Non-Spherical Fine
Enhanced Signal | Non Enhanced Signal | Same intensity as 532 | Spherical Coarse
Enhanced Signal | Non Enhanced Signal | Lower intensity than 532 | Spherical Fine

## Slide 23: CALIPSO browse images online
A
B
A
B
Level 1 products
If same intensity in both channels, coarse particles
If signal more intense in β’532, fine particles
Region A: coarse non spherical
= cirrus cloud?
Region B: fine spherical
= urban pollution?
Total attenuated backscatter 532 nm
Total attenuated backscatter 1064 nm

## Slide 24: Example: June 26, 2006
0-km
5-km
10-km
15-km
20-km
45° N
40° N
35° N
30° N
25° N
20° N
15° N
Total attenuated backscatter 532 nm
Parallel channel enhanced?
Signal also strong in 1064?

## Slide 25: Example: June 26, 2006
0-km
5-km
10-km
15-km
20-km
45° N
40° N
35° N
30° N
25° N
20° N
15° N
Total attenuated backscatter 532 nm
=>Most probably dust
Non spherical
Coarse particles

## Slide 26: CALIPSO browse images online
Level 2 products
aerosol (B)
cloud (A)
clear air
A
B
clean marine
dust (B)
polluted continental
clean continental
polluted dust (B)
smoke
B
According to Level 2,
Region A: cloud
Region B: dust/ polluted dust for B
Vertical Feature Mask
Aerosol Sub-type
Different from Level 1 Analysis…

## Slide 27: Which data should I use?
Safest is qualitative use of level 1 latest version (currently 4) attenuated backscatter data in 3 channels
 Browse standard product lidar images online
For quantitative use, level 1 data contains less uncertainties than level 2 data
If you use level 2 data, you need to know the associated uncertainties (and most of these are reported in the level 2 data products)
Some knowledge on Level 1-to-level 2 algorithm…

## Slide 28: Level 1-to-level 2 algorithm
Averaging engine
Profile Scanner
Extinction Averaging Engine
Profile Solver
T2 corrected layer properties
Vertical Feature Mask
1/3km Cloud Layer Product
1km Cloud Layer Product
5km Cloud Layer Product
5km Aerosol Layer Product
5km Cloud Profile Product
5km Aerosol Profile Product
Scene Classification Algorithm
Composite layer Product
Preliminary Profile Product
Profile Averaging engine
Input (level 1, β’)
Output (level 2)
1. Layer detection
2. Layer classification
3. Layer extinction
Combined aerosol and cloud layer

## Slide 29: Layer Detection
b) Data averaged from 333m to 5km
d) Detected layers removed from curtain scene
e) Further averaging of the data (20, 80km)…
c) Layers identified as enhancements above molecular background (adaptive threshold using β’532,⊥and β’532,// and molecular model)
Here cloud detected at 333m; aerosol at 5km
a) Input is level 1 attenuated backscatter

## Slide 30: Example: June 26, 2006
0-km
5-km
10-km
15-km
20-km
45° N
40° N
35° N
30° N
25° N
20° N
15° N
N/A single shot 1-km 5-km 20-km 80-km
Different amounts of horizontal averaging are required to detect different portions of the dust layer

## Slide 31: Example: June 26, 2006
0-km
5-km
10-km
15-km
20-km
45° N
40° N
35° N
30° N
25° N
20° N
15° N
invalid clear cloud aerosol stratospheric surface subsurface no signal
Cloud-Aerosol Discrimination

## Slide 32: Example: June 26, 2006
dust
polluted continental
polluted dust
smoke
Aerosol sub-typing

## Slide 33: CALIPSO: example of application
The detection of aerosols over clouds
Aerosols and their radiative effects are a major uncertainty in predictions of future climate change
Biomass burning aerosols usually strongly absorbing, may cause local positive radiative forcing when over clouds
CALIOP is the only satellite sensor capable of observing aerosol over clouds without any auxiliary data (OMI or POLDER need to combine with MODIS and/ or CALIOP)
Before studying aerosol radiative effects over clouds, we need to know where and when aerosol over clouds occur as well as their intensity
We use the CALIPSO level 2 aerosol layer product…

## Slide 34: Aerosol Over Cloud (AOC)
Over 50 % AOC (/CALIOP data) offshore from South America and South Africa
Probably mostly biomass burning smoke
“…huge increase in fire activity in 2007… largest over the last ten years” and “largest 6-month (May–October) precipitation deficit of the last ten years in South America occurred during 2007 [Torres et al., 2009]
October 2007 AOC occurrence
October 2007 MODIS active fires

## Slide 35: Take home message
CALIOP/ CALIPSO provides aerosol vertical distribution and info on type of particle (size and shape)
Safest use of CALIOP data:
Qualitative (browse lidar images online)
Latest version (currently V3.01)
Level 1 (contains less uncertainties than level 2 data)
Concerning the use of CALIOP Level 2 data,
recognize the unvalidated nature of the data
keep in mind the uncertainties
make sure to read all quality assurance information and to apply the appropriate quality flags (see user guide, http://www-calipso.larc.nasa.gov/resources/calipso_users_guide/)
If you have any concerns, ask the CALIPSO team

## Slide 36: Online
User Guide:
  http://www-calipso.larc.nasa.gov/resources/calipso_users_guide/
  FAQ, Essential reading, Data Product Descriptions, Data quality summaries (V3.3), Example and tools, Order Data, Publications
Data download
  https://eosweb.larc.nasa.gov/HORDERBIN/HTML_Start.cgi
  http://www-calipso.larc.nasa.gov/search/ for subset files
LIDAR browse images
Level 1 and Level 2 Vertical Feature Mask; No level 2 profile
  EXPEDITED 12h-RELEASE with kmz files
  http://www-calipso.larc.nasa.gov/products/lidar/browse_images/expedited/
  STANDARD PRODUCT for detailed science analysis
  http://www-calipso.larc.nasa.gov/products/lidar/browse_images/show_calendar.php/
  Also provides horizontal averaging, Ice/ Water phase and aerosol subtype
*Note they’re doing maintanence on their websites right now

## Slide 37: Data Access Interface
You need to know
  Project = CALIPSO
  Parameter
    e.g. Variety including 532nm backscatter coefficient
  Data Set
    Different data sets, processed with different version of the algorithm.
    Current Version is ValStage 1 3.40 for Level 1 data and Level 2 data like the virtual feature mask
  Time Frame
    Remember it went up in 2006